## Slide 1: 2025-05-23 Update

## Slide 2: Compression Tester
Controller runs “NI-Linux”
  Has an exposed ssh service
    User: “admin”, Password: “admin”
  Weird Silverlight web ui
Communication is done over TCP packets, we could try to reverse engineer but it would be very time consuming
Apparently there is an api for LabVIEW? But it costs like $7000
Thought it might work as an NI DAQ network device (which there is a python library for) but apparently not
Customer support doesn’t want to help us bypass their sofware

## Slide 3: Compression Tester (cont.)
Worst solution is a script on the laptop that drags the mouse around blindly
The compression tester was already set up to give an output to the Arduino when a test was running, but IIRC we can’t start the test from the Arduino
This compression tester was really not made to be automated

## Slide 4: Git
OpenTrons doesn’t have an internet connection at the moment so that won’t work
  Is there some reason why it shouldn’t?
But it would be nice
Also what weird distro of linux is the raspi running
  it’s some weird embedded distro but I don’t see a package manager so not sure if we can even install git (just load the binary on directly I guess)
The OpenTrons has a raspi in it (it’s a computer) but it’s meant to act like a device instead

## Slide 5: Plan
If possible, get the OpenTrons on the internet so it can pull directly from the git repo
Refactor the code into separate files instead of one big jupyter notebook
Potentially look into writing a REST api or similar that runs on the Newton controller (compression tester)
  Embedded NI-Linux seems to run a version of LabVIEW RealTime, so might be able to work with that
  Alternatively look into reverse engineering the communication from the official Newton software